## Slide 1: Mechanical Advantage
What do simple machines do for us anyway?

## Slide 2: There are four ways that a machine helps us to do work.
Transfers our effort force from one place to another. Ex: seesaw
Multiply your effort force. Ex: crowbar
Magnify speed and distance. Ex: baseball bat
Changing the direction of the force. Ex: pulley on the flagpole

## Slide 3: Mechanical Advantage
The number of times a machine multiplies your effort force.
  Example: If you push on the handle of a car jack with a force of 30 lbs and the jack lifts a 3000 lb car, what is the jack’s mechanical advantage?
  The jack multiplies your effort force by 100 times.

## Slide 4: There are 2 types of mechanical advantage.
IMA – Ideal mechanical advantage.
This is the number of times a machine is designed to multiply your effort force.
It is based on measurements of the machine.
Ignores friction
AMA – Actual mechanical advantage
This is the number of times the machine actually multiplies your effort force.
AMA = resistance force/effort force.
Includes the effects of friction
IMA is always larger than AMA.

## Slide 5: There are 3 Classes of Levers
Depends on the location of 3 items:
1. Fulcrum – fixed point on a lever
2. Effort Arm – the part of the lever that exerts the effort force.
3. Resistance Arm – the part of the lever that exerts the resistance force.
 EA 
RA

## Slide 6: 1st Class Lever
  Changes the direction of the force
  Multiplies effort force
  Magnifies speed and distance
  Ex: seesaw, crowbar, scissors

## Slide 7: 2nd Class Lever
  Multiply effort force
  Mechanical advantage is always greater than 1.
  Ex: bottle opener, boat oars, wheel barrow

## Slide 8: 3rd Class Lever
  Magnifies speed and distance
  Mechanical Advantage always less than 1
  Ex: baseball bat, golf club, broom, shovel

## Slide 11: 1. What is the IMA of this pulley system? 2. Ignoring friction, if you want to lift the resistance 3 meters what will the effort distance be? 3. Ignoring friction how much effort force will be necessary to lift a load of 15 newtons? 4. How much work is done?